## Slide 1
RESULTS AND CONCLUSIONS
The robotic system will undergo a series of tests, including the evaluation of the mapping and navigation algorithm, verifying whether it is able to deviate from obstacles, assessing the effectiveness of coupling the robot to the wheelchair, as well as the autonomy of the robot and the robot safety system developed for emergency situations. Finally, transport time, as well as its efficiency and error in a set of tests, will also be analyzed.
In a way, the expected result of this project will be a robotic system based in ROS to assist in the management of wheelchair transportation in health institutions, increasing their availability and reducing the time needed for medical staff in these tasks.
BACKGROUND
Industry 4.0 presents itself as a new era in which the industry is led by technologies such as robotics, artificial intelligence, and device interconnection (IIoT). The increasing implementation of robots in industries allows for a better quality of service with high accuracy in less time. As a result, these advantages are now in other areas such as medicine or the military to mitigate problems.
In healthcare institutions, the transport of patients is a recurrent, time-consuming, non-ergonomic task and requires the help of assistants. There are solutions such as electric wheelchairs that facilitate patient motion or intelligent wheelchairs that transport patients to their destination autonomously, however, their costs are high, and replacing them with these chairs requires a huge financial effort from the institutions.
This robotic system can play an extremely important role both at a scientific and social level. At the scientific level, the transport of patients autonomously through a robot in hospital environments, for example, can be validated, and perhaps in the future the adaptation to the transport of hospital equipment. At the social level, it will allow health institutions to reduce costs since a robot allows the transport of multiple manual wheelchairs, taking full advantage of the current fleets of manual wheelchairs.
OBJECTIVES
The objective of this project is to develop a robotic system capable of transporting conventional wheelchairs existing in health institutions and through communication with the management system of the institution streamline the entire transport process, making it safe, fast, and comfortable for all intervening.
BIBLIOGRAPHY
AUTONOMOUS MOBILE ROBOT FOR WHEELCHAIRS TRANSPORTATION IN HEALTHCARE INSTITUTIONS
João Faria
Master in Electronics and Computing Engineering
António Moreira
METHODOLOGY
This project consists of developing a robotic system capable of transporting patients in manual wheelchairs in health institutions. Therefore, the system will have to have a coupling mechanism to the self-contained chair, easy to fit, fast and universal, since there is a high diversity of chairs. The initial plan is to integrate the coupling system with an existing robot. The coupling system will have to be studied, however, there are already some idealized approaches, Figure 1. The approach that presents greater ease of construction and implementation is the second approach, Figure 1 (b), however, the rest will also be evaluated.
In any of the coupling approaches a camera and a microcontroller will be used. The main function of the assembly is to discover the coupling points of the manual wheelchair and move the claw to attach to the chair. For docking to be fast, safe, and effective, it may be necessary to implement a deep learning algorithm for sorting or detaining objects. As a robot safety system during transport will be implemented a set of sensors to monitor the patient and can act in emergency situations.
Finally, an application will be developed where nurses and doctors will be allowed to request transport to the AMR robot. An interface will also allow communication with the information management system of the health institution to know which transport, who requested transportation, among other information.
Communication with the institution's management system is essential, as sometimes transportation involves a change of floor and, thus, access to elevators is mandatory, since destination may be as diverse as cafeterias, areas of treatment or diagnostic, outdoor, etc. It will also be studied the fact that there is a transporter robot for each floor of the building to see if it adds advantages to management.
The integration with the information management system of the institution will be a complex process since it requires a partnership with the company. If it is not possible it will be simulated.
[1] S. Y. Lee, S. C. Kim, M. H. Lee, and Y. I. Lee, “Comparison of shoulder and back muscle activation in caregivers according to various handle heights,” Journal of Physical Therapy Science, vol. 25, no. 10. pp. 1231–1233, 2013. doi: 10.1589/jpts.25.1231.
[2] O. Mazumder, A. S. Kundu, R. Chattaraj, and S. Bhaumik, “Holonomic wheelchair control using EMG signal and joystick interface,” 2014 Recent Adv. Eng. Comput. Sci. RAECS 2014, pp. 6–8, 2014, doi: 10.1109/RAECS.2014.6799574.
[3] A. R. Baltazar, M. R. Petry, M. F. Silva, and A. P. Moreira, “Autonomous wheelchair for patient’s transportation on healthcare institutions,” SN Appl. Sci., vol. 3, no. 3, pp. 1–13, 2021, doi: 10.1007/s42452-021-04304-1.
[4] Z. Dai, C. Du, Z. Chen, M. Yuan, and G. Peng, “Design of a New Type of External Traction Device of Wheelchair based on STM32 Chip,” J. Phys. Conf. Ser., vol. 1176, no. 5, 2019, doi: 10.1088/1742-6596/1176/5/052050.
CONTACTS
João Faria - a14861@alunos.ipca.pt (student)
António Moreira - amoreira@ipca.pt (supervisor 1)
(a)
(b)
(c)
Figure 1 – Types of boarding from a manual wheelchair to a robot. (a) Central coupling; (b) Coupling from below; (c) Impeller coupling.
AMR robot
Wheelchair + patient + safety system
Coupling system
Health institution management system
Human Machine Interface
Figure 2 – General diagram.
Manual Wheelchair Transporter Robot

## Slide 2
RESULTS AND CONCLUSIONS
The robotic system will undergo a series of tests, such as evaluating the effectiveness of the robot safety system developed for emergency situations and analyzing the transport time as well as its efficiency and error in a set of tests.
In a way, the expected result of this project will be the development of a robotic system, safe and effective, to transport manual wheelchairs and assist in the management of patient transport in health institutions.
BACKGROUND
OBJECTIVES
Industry 4.0 presents itself as a new era in which the industry is led by technologies such as robotics, artificial intelligence, and device interconnection (IIoT). The increasing implementation of robots in industries allows a better quality of service with high accuracy in less time. As a result, these advantages are now in other areas such as medicine or the military to mitigate problems.
In healthcare institutions, the transport of patients is a recurrent, time-consuming, non-ergonomic task and requires the help of assistants. There are solutions such as electric wheelchairs that facilitate patient motion or intelligent wheelchairs that transport patients to their destination autonomously, however, their costs are high, and replacing them with these chairs requires a huge financial effort from the institutions.
This service system can play an extremely important role both at the scientific and social levels. At the scientific level, the transport of patients autonomously through a robot in hospital environments, for example, can be validated, and perhaps in the future the adaptation to the transport of hospital equipment. At the social level, allowing health institutions to reduce costs since they can carry out the transport of guardianship patients as conventional wheelchairs.
METHODOLOGY
This project is divided into Human Machine interface and consists of the application or website that allows giving transport orders to the AMR robot, in the management system of the health institution where it has stored all the information of the institution, such as users and spaces, and finally the wheelchair transport robot whose main function is to carry out the transport quickly and safely. The coupling system will have to be studied, however, there are already some idealized approaches, Figure 1. For the development of the coupling system will be used a camera and a microcontroller, whose main function is to discover the coupling points of the wheelchair and move the claw to fix to the chair.
The integration with the institution's information management system will be a complex process since it requires a partnership with the company. If it is not possible, it will be simulated.
The objective of this project is to develop a robotic system capable of transporting conventional wheelchairs existing in health institutions and through communication with the management system of the institution streamline the entire transport process, making it safe, fast, and comfortable for all intervening.
BIBLIOGRAPHY
AUTONOMOUS MOBILE ROBOT FOR WHEELCHAIRS TRANSPORTATION IN HEALTHCARE INSTITUTIONS
João Faria
Master in Electronics and Computing Engineering
António Moreira
[1] S. Y. Lee, S. C. Kim, M. H. Lee, and Y. I. Lee, “Comparison of shoulder and back muscle activation in caregivers according to various handle heights,” Journal of Physical Therapy Science, vol. 25, no. 10. pp. 1231–1233, 2013. doi: 10.1589/jpts.25.1231.
[2] O. Mazumder, A. S. Kundu, R. Chattaraj, and S. Bhaumik, “Holonomic wheelchair control using EMG signal and joystick interface,” 2014 Recent Adv. Eng. Comput. Sci. RAECS 2014, pp. 6–8, 2014, doi: 10.1109/RAECS.2014.6799574.
[3] A. R. Baltazar, M. R. Petry, M. F. Silva, and A. P. Moreira, “Autonomous wheelchair for patient’s transportation on healthcare institutions,” SN Appl. Sci., vol. 3, no. 3, pp. 1–13, 2021, doi: 10.1007/s42452-021-04304-1.
[4] Z. Dai, C. Du, Z. Chen, M. Yuan, and G. Peng, “Design of a New Type of External Traction Device of Wheelchair based on STM32 Chip,” J. Phys. Conf. Ser., vol. 1176, no. 5, 2019, doi: 10.1088/1742-6596/1176/5/052050.
CONTACTS
João Faria - jpfaria@ipca.pt (student)
António Moreira - amoreira@ipca.pt (supervisor 1)
The application where nurses and doctors will be able to request the transport of the AMR robot.
Health Institution Management System
Communication with the institution's institutional system is essential to know information such as: which patient is transported, who requests transport, and the various destinations such as treatment or diagnostic areas, outdoors, etc.
AMR robot
Coupling system
Wheelchair Transporter Robot
Wheelchair + patient +
safety system
Type of transport
Used to attach the coupling system.
Implementation of a security system consisting of a set of sensors to monitor the patient and act in emergency situations.
Impeller coupling – pushing the wheelchair
Central coupling – pulling the wheelchair
Coupling from below – lifting the wheelchair
Human Machine Interface
Figure 1 – General diagram.
Easy-to-fit, fast, autonomous, and universal coupling mechanism, because there is a diversity of wheelchairs.

## Slide 3
RESULTS AND CONCLUSIONS
The robotic system will undergo a series of tests, such as evaluating the effectiveness of the robot safety system developed for emergency situations and analyzing the transport time as well as its efficiency and error in a set of tests.
In a way, the expected result of this project will be the development of a robotic system, safe and effective, to transport manual wheelchairs and assist in the management of patient transport in health institutions.
BACKGROUND
OBJECTIVES
Industry 4.0 presents itself as a new era in which the industry is led by technologies such as robotics, artificial intelligence, and device interconnection (IIoT). The increasing implementation of robots in industries allows a better quality of service with high accuracy in less time. As a result, these advantages are now in other areas such as medicine or the military to mitigate problems.
In healthcare institutions, the transport of patients is a recurrent, time-consuming, non-ergonomic task and requires the help of assistants. There are solutions such as electric wheelchairs that facilitate patient motion or intelligent wheelchairs that transport patients to their destination autonomously, however, their costs are high, and replacing them with these chairs requires a huge financial effort from the institutions.
This service system can play an extremely important role both at the scientific and social levels. At the scientific level, the transport of patients autonomously through a robot in hospital environments, for example, can be validated, and perhaps in the future the adaptation to the transport of hospital equipment. At the social level, allowing health institutions to reduce costs since they can carry out the transport of guardianship patients as conventional wheelchairs.
METHODOLOGY
This project, Figure 1, is divided into three phases:
Human Machine interface consists of the application or website that allows giving transport orders to the AMR robot;
Management system of the health institution where it has stored all the information of the institution, such as users and spaces;
Wheelchair transport robot whose main function is to carry out the transport quickly and safely. The coupling system will have to be studied and for the development of the coupling system will be used a camera and a microcontroller, whose main function is to discover the coupling points of the wheelchair and move the claw to fix to the chair.
The integration with the institution's information management system will be a complex process since it requires a partnership with the institution. If it is not possible, it will be simulated.
The objective of this project is to develop a robotic system capable of transporting conventional wheelchairs existing in health institutions and through communication with the management system of the institution streamline the entire transport process, making it safe, fast, and comfortable for all intervening.
BIBLIOGRAPHY
AUTONOMOUS MOBILE ROBOT FOR WHEELCHAIRS TRANSPORTATION IN HEALTHCARE INSTITUTIONS
João Faria
Master in Electronics and Computing Engineering
António Moreira
[1] S. Y. Lee, S. C. Kim, M. H. Lee, and Y. I. Lee, “Comparison of shoulder and back muscle activation in caregivers according to various handle heights,” Journal of Physical Therapy Science, vol. 25, no. 10. pp. 1231–1233, 2013. doi: 10.1589/jpts.25.1231.
[2] O. Mazumder, A. S. Kundu, R. Chattaraj, and S. Bhaumik, “Holonomic wheelchair control using EMG signal and joystick interface,” 2014 Recent Adv. Eng. Comput. Sci. RAECS 2014, pp. 6–8, 2014, doi: 10.1109/RAECS.2014.6799574.
[3] A. R. Baltazar, M. R. Petry, M. F. Silva, and A. P. Moreira, “Autonomous wheelchair for patient’s transportation on healthcare institutions,” SN Appl. Sci., vol. 3, no. 3, pp. 1–13, 2021, doi: 10.1007/s42452-021-04304-1.
[4] Z. Dai, C. Du, Z. Chen, M. Yuan, and G. Peng, “Design of a New Type of External Traction Device of Wheelchair based on STM32 Chip,” J. Phys. Conf. Ser., vol. 1176, no. 5, 2019, doi: 10.1088/1742-6596/1176/5/052050.
CONTACTS
João Faria - jpfaria@ipca.pt (student)
António Moreira - amoreira@ipca.pt (supervisor 1)
The application where nurses and doctors will be able to request the transport of the AMR robot.
2. Health Institution Management System
Communication with the institution's institutional system is essential to know information such as: which patient is transported, who requests transport, and the various destinations such as treatment or diagnostic areas, outdoors, etc.
AMR robot
Coupling system
3. Wheelchair Transporter Robot
Wheelchair + patient +
safety system
Type of transport
Used to attach the coupling system.
Implementation of a security system consisting of a set of sensors to monitor the patient and act in emergency situations.
Impeller coupling – pushing the wheelchair
Central coupling – pulling the wheelchair
Coupling from below – lifting the wheelchair
1. Human Machine Interface
Figure 1 – General diagram.
Easy-to-fit, fast, autonomous, and universal coupling mechanism, because there is a diversity of wheelchairs.

## Slide 4
RESULTS AND CONCLUSIONS
The robotic system will undergo a series of tests, such as evaluating the effectiveness of the robot safety system developed for emergency situations and analyzing the transport time as well as its efficiency and error in a set of tests.
In a way, the expected result of this project will be the development of a robotic system, safe and effective, to transport manual wheelchairs and assist in the management of patient transport in health institutions.
BACKGROUND
OBJECTIVES
Industry 4.0 presents itself as a new era in which the industry is led by technologies such as robotics, artificial intelligence, and device interconnection (IIoT). The increasing implementation of robots in industries allows a better quality of service with high accuracy in less time. As a result, these advantages are now in other areas such as medicine or the military to mitigate problems.
In healthcare institutions, the transport of patients is a recurrent, time-consuming, non-ergonomic task and requires the help of assistants [1]. There are solutions such as electric wheelchairs [2] that facilitate patient motion or intelligent wheelchairs [3] that transport patients to their destination autonomously, however, their costs are high, and replacing them with these chairs requires a huge financial effort from the institutions.
This service system can play an extremely important role both at the scientific and social levels. At the scientific level, the transport of patients autonomously through a robot in hospital environments, for example, can be validated, and perhaps in the future the adaptation to the transport of hospital equipment. At the social level, allowing health institutions to reduce costs since they can carry out the transport of guardianship patients as conventional wheelchairs.
METHODOLOGY
This project, Figure 1, is divided into three parts:
Human Machine interface consists of the application or website that allows giving transport orders to the AMR robot;
Management system of the health institution where it has stored all the information of the institution, such as users and spaces;
Wheelchair transport robot whose main function is to carry out the transport quickly and safely. The coupling system will have to be studied and for the development of the coupling system will be used a camera and a microcontroller, whose main function is to discover the coupling points of the wheelchair and move the claw to fix to the chair.
The integration with the institution's information management system will be a complex process since it requires a partnership with the institution. If it is not possible, it will be simulated.
The objective of this project is to develop a robotic system capable of transporting conventional wheelchairs existing in health institutions and through communication with the management system of the institution streamline the entire transport process, making it safe, fast, and comfortable for all intervening.
BIBLIOGRAPHY
AUTONOMOUS MOBILE ROBOT FOR WHEELCHAIRS TRANSPORTATION IN HEALTHCARE INSTITUTIONS
João Faria
Master in Electronics and Computing Engineering
António Moreira
[1] S. Y. Lee, S. C. Kim, M. H. Lee, and Y. I. Lee, “Comparison of shoulder and back muscle activation in caregivers according to various handle heights,” Journal of Physical Therapy Science, vol. 25, no. 10. pp. 1231–1233, 2013. doi: 10.1589/jpts.25.1231.
[2] O. Mazumder, A. S. Kundu, R. Chattaraj, and S. Bhaumik, “Holonomic wheelchair control using EMG signal and joystick interface,” 2014 Recent Adv. Eng. Comput. Sci. RAECS 2014, pp. 6–8, 2014, doi: 10.1109/RAECS.2014.6799574.
[3] A. R. Baltazar, M. R. Petry, M. F. Silva, and A. P. Moreira, “Autonomous wheelchair for patient’s transportation on healthcare institutions,” SN Appl. Sci., vol. 3, no. 3, pp. 1–13, 2021, doi: 10.1007/s42452-021-04304-1.
[4] Z. Dai, C. Du, Z. Chen, M. Yuan, and G. Peng, “Design of a New Type of External Traction Device of Wheelchair based on STM32 Chip,” J. Phys. Conf. Ser., vol. 1176, no. 5, 2019, doi: 10.1088/1742-6596/1176/5/052050.
CONTACTS
João Faria - jpfaria@ipca.pt (student)
António Moreira - amoreira@ipca.pt (supervisor 1)
The application where nurses and doctors will be able to request the transport of the AMR robot.
2. Health Institution Management System
Communication with the institution's institutional system is essential to know information such as: which patient is transported, who requests transport, and the various destinations such as treatment or diagnostic areas, outdoors, etc.
AMR robot
Coupling system
3. Wheelchair Transporter Robot
Wheelchair + patient +
safety system
Type of transport
Used to attach the coupling system.
Implementation of a security system consisting of a set of sensors to monitor the patient and act in emergency situations.
Impeller coupling – pushing the wheelchair
Central coupling – pulling the wheelchair
Coupling from below – lifting the wheelchair
1. Human Machine Interface
Figure 1 – General diagram.
Easy-to-fit, fast, autonomous, and universal coupling mechanism, because there is a diversity of wheelchairs [4].

## Slide 5
RESULTS AND CONCLUSIONS
The robotic system will undergo a series of tests, such as evaluating the effectiveness of the robot safety system developed for emergency situations and analyzing the transport time, as well as, its efficiency and error in a set of tests/tasks.
In a way, the expected result of this project will be the development of a robotic system, safe and effective, to transport manual wheelchairs and assist in the management of patient transport in health institutions.
BACKGROUND
OBJECTIVES
Industry 4.0 presents itself as a new era in which the industry is led by technologies such as robotics, artificial intelligence and the internet of things (IoT). The increasing implementation of robots in industries allows a better quality of service with high accuracy in less time. As a result, these advantages are now in other areas such as medicine or the military to mitigate problems.
In healthcare institutions, the transport of patients is a recurrent, time-consuming, non-ergonomic task and requires the help of assistants [1]. There are solutions such as electric wheelchairs [2] that facilitate patient motion or intelligent wheelchairs [3] that transport patients to their destination autonomously, however, their costs are high, and replacing them with these chairs requires a huge financial effort from the institutions.
This service system can play an extremely important role both at the scientific and social levels. At the scientific level, the transport of patients autonomously through a robot in hospital environments, for example, can be validated, and perhaps in the future the adaptation to the transport of hospital equipment. At the social level, allowing health institutions to reduce costs since they can carry out the transport of guardianship patients as conventional wheelchairs.
METHODOLOGY
This project, Figure 1, is divided into three parts:
A Human Machine interface consisting in an application or website that allows giving transport orders to the AMR robot;
Connection with the management system of the health institution where it has stored all the information of the institution, such as users and spaces;
Robotic Wheelchair transport whose main function is to carry out the wheelchairs quickly and safely. The coupling system will have to be studied and for the development of this, one will explore cameras and a microcontrollers, whose main function is to discover the coupling points of the wheelchair and move the claw to fix to the chair.
The integration with the institution's information management system will be a complex process since it requires a partnership with the institution. If it is not possible, it will be simulated.
The objective of this project is to develop a robotic system capable of transporting conventional wheelchairs existing in health institutions and through communication with the management system of the institution streamline the entire transport process, making it safe, fast, and comfortable for all intervening.
BIBLIOGRAPHY
AUTONOMOUS MOBILE ROBOT FOR WHEELCHAIRS TRANSPORTATION IN HEALTHCARE INSTITUTIONS
João Faria
Master in Electronics and Computing Engineering
António Moreira
[1] S. Y. Lee, S. C. Kim, M. H. Lee, and Y. I. Lee, “Comparison of shoulder and back muscle activation in caregivers according to various handle heights,” Journal of Physical Therapy Science, vol. 25, no. 10. pp. 1231–1233, 2013. doi: 10.1589/jpts.25.1231.
[2] O. Mazumder, A. S. Kundu, R. Chattaraj, and S. Bhaumik, “Holonomic wheelchair control using EMG signal and joystick interface,” 2014 Recent Adv. Eng. Comput. Sci. RAECS 2014, pp. 6–8, 2014, doi: 10.1109/RAECS.2014.6799574.
[3] A. R. Baltazar, M. R. Petry, M. F. Silva, and A. P. Moreira, “Autonomous wheelchair for patient’s transportation on healthcare institutions,” SN Appl. Sci., vol. 3, no. 3, pp. 1–13, 2021, doi: 10.1007/s42452-021-04304-1.
[4] Z. Dai, C. Du, Z. Chen, M. Yuan, and G. Peng, “Design of a New Type of External Traction Device of Wheelchair based on STM32 Chip,” J. Phys. Conf. Ser., vol. 1176, no. 5, 2019, doi: 10.1088/1742-6596/1176/5/052050.
CONTACTS
João Faria - jpfaria@ipca.pt (student)
António Moreira - amoreira@ipca.pt (supervisor 1)
The application where nurses and doctors will be able to request the transport of the AMR robot.
2. Health Institution Management System
Communication with the institution's institutional system is essential to know information such as: which patient is transported, who requests transport, and the various destinations such as treatment or diagnostic areas, outdoors, etc.
AMR robot
Coupling system
3. Wheelchair Transporter Robot
Wheelchair + patient +
safety system
Type of transport
Used to attach the coupling system.
Implementation of a security system consisting of a set of sensors to monitor the patient and act in emergency situations.
Impeller coupling – pushing the wheelchair
Central coupling – pulling the wheelchair
Coupling from below – lifting the wheelchair
1. Human Machine Interface
Figure 1 – General diagram.
Easy-to-fit, fast, autonomous, and universal coupling mechanism, because there is a diversity of wheelchairs [4].

## Slide 6
TESTS AND OUTCOMES
BACKGROUND
OBJECTIVES
Industry 4.0 presents itself as a new era in which the industry is led by technologies such as robotics, artificial intelligence, and the internet of things (IoT). The increasing implementation of robots in industries allows a better quality of service with high accuracy in less time. As a result, these advantages are now in other areas such as medicine or the military to mitigate problems.
In healthcare institutions, the transport of patients is a recurrent, time-consuming, non-ergonomic task and requires the help of assistants [1]. There are solutions such as electric wheelchairs [2] that facilitate patient motion or intelligent wheelchairs [3] that transport patients to their destination autonomously, however, their costs are high, and replacing them with these chairs requires a huge financial effort from the institutions.
This service system can play an extremely important role both at the scientific and social levels. At the scientific level, the transport of patients autonomously through a robot in hospital environments, for example, can be validated, and perhaps in the future the adaptation to the transport of hospital equipment. At the social level, allowing health institutions to reduce costs since they can carry out the transport of guardianship patients as conventional wheelchairs.
METHODOLOGY
This project, Figure 1, is divided into three parts:
A Human Machine interface consisting in an application or website that allows giving transport orders to the AMR robot;
Connection with the management system of the health institution where it has stored all the information of the institution, such as users and spaces;
Robotic Wheelchair transport whose main function is to carry out the wheelchairs quickly and safely. The coupling system will have to be studied and for the development of this, one will explore cameras and a microcontrollers, whose main function is to discover the coupling points of the wheelchair and move the claw to fix to the chair.
The integration with the institution's information management system will be a complex process since it requires a partnership with the institution. If it is not possible, it will be simulated.
The objective of this project is to develop a robotic system capable of transporting conventional wheelchairs existing in health institutions and through communication with the management system of the institution streamline the entire transport process, making it safe, fast, and comfortable for all intervening.
BIBLIOGRAPHY
AUTONOMOUS MOBILE ROBOT FOR WHEELCHAIRS TRANSPORTATION IN HEALTHCARE INSTITUTIONS
João Faria
Master in Electronics and Computing Engineering
António Moreira
[1] S. Y. Lee, S. C. Kim, M. H. Lee, and Y. I. Lee, “Comparison of shoulder and back muscle activation in caregivers according to various handle heights,” Journal of Physical Therapy Science, vol. 25, no. 10. pp. 1231–1233, 2013. doi: 10.1589/jpts.25.1231.
[2] O. Mazumder, A. S. Kundu, R. Chattaraj, and S. Bhaumik, “Holonomic wheelchair control using EMG signal and joystick interface,” 2014 Recent Adv. Eng. Comput. Sci. RAECS 2014, pp. 6–8, 2014, doi: 10.1109/RAECS.2014.6799574.
[3] A. R. Baltazar, M. R. Petry, M. F. Silva, and A. P. Moreira, “Autonomous wheelchair for patient’s transportation on healthcare institutions,” SN Appl. Sci., vol. 3, no. 3, pp. 1–13, 2021, doi: 10.1007/s42452-021-04304-1.
[4] Z. Dai, C. Du, Z. Chen, M. Yuan, and G. Peng, “Design of a New Type of External Traction Device of Wheelchair based on STM32 Chip,” J. Phys. Conf. Ser., vol. 1176, no. 5, 2019, doi: 10.1088/1742-6596/1176/5/052050.
CONTACTS
João Faria - jpfaria@ipca.pt (student)
António Moreira - amoreira@ipca.pt (supervisor 1)
The application where nurses and doctors will be able to request the transport of the AMR robot.
2. Health Institution Management System
Communication with the institution's institutional system is essential to know information such as: which patient is transported, who requests transport, and the various destinations such as treatment or diagnostic areas, outdoors, etc.
AMR robot
Coupling system
3. Wheelchair Transporter Robot
Wheelchair + patient +
safety system
Type of transport
Used to attach the coupling system.
Implementation of a security system consisting of a set of sensors to monitor the patient and act in emergency situations.
Impeller coupling – pushing the wheelchair
Central coupling – pulling the wheelchair
Coupling from below – lifting the wheelchair
1. Human Machine Interface
Figure 1 – General diagram.
Easy-to-fit, fast, autonomous, and universal coupling mechanism, because there is a diversity of wheelchairs [4].
Tests
Evaluation of the performance of the chair coupling system, coupling effectiveness;
Evaluation of the efficiency of the patient safety system;
Evaluation of efficiency and the whole system as well as the transport time in a set of tests.
Development of a robotic system based in ROS to assist in the management of wheelchair transportation in health institutions, increasing their availability and reducing the time needed for medical staff in these tasks.
Outcomes